S1: Stadium Roof Design – Design Decisions

Top 6 Biggest stadium in the UK?

- ……………………………………………………….

- ……………………………………………………….

- ……………………………………………………….

- ……………………………………………………….

- ……………………………………………………….

- ……………………………………………………….

What groups of people would you need to consider when designing a stadium?

Client Brief Exercise

As a Spectator or a Owner/Operator or a Participant discuss

|  | How does the design of the roof affect this need/want? |
| --- | --- |
| Your needs – What is absolutely essential for the stadium to work for you |  |
| Your wants – What would the added bonus’s be |  |

Design Brief for the roof:-

Design Decisions Exercise

In groups of three containing one spectator, one participant and one owner/operator, try to design the most cost effective stadium.

You need to choose a roof type, a degree of enclosure, a system for good quality grass and a roof covering material.

You want to maximise the different between the cost and the value added.

|  | Cost (£million) | Value Added (£million) |
| --- | --- | --- |
| Roof Type |  | Individuality | Ability to save energy on lighting | Ability to blend into surrounds | Ease of Maintenance | Ease of construction |
| Goal post structures | 40 | 10 | 2 | 15 | 2 | 25 |
| Cantilever Roof | 60 | 40 | 5 | 4 | 15 | 23 |
| Space frame structure | 75 | 50 | 8 | 8 | 10 | 8 |
| Tension Structure | 80 | 45 | 10 | 20 | 8 | 7 |
| Degree of Enclosure |  | Flexibility | Construction Time | Atmosphere | Comfort |  |
| No roof | 30 | 5 | 15 | 2 | 1 |  |
| Fixed covering for spectators | 75 | 40 | 10 | 35 | 15 |  |
| Retractable Roof | 150 | 100 | 2 | 40 | 25 |  |
| Completely enclosed stadium | 130 | 50 | 8 | 50 | 30 |  |
| System for good quality grass |  | Quality of grass | Flexibility |  |
| Roll-In, Roll-out pitch | 50 | 40 | 40 |  |
| Pitch that can be raised to roof level | 75 | 35 | 0 |  |
| Permanent in situ pitch | 10 | 15 | 0 |  |
| Roof covering material |  | Quality of grass |  |
| Opaque | 10 | 5 |  |
| Translucent | 15 | 25 |  |
| Combination | 20 | 20 |  |
|  | Choice | Total Value Added | Cost | Difference (Value added – Cost) |
| Roof Type |  |  |  |  |
| Degree of Enclosure |  |  |  |  |
| System for grass |  |  |  |  |
| Roof Covering |  |  |  |  |

|  | Choice | Total Value Added | Cost | Difference (Value added – Cost) |
| --- | --- | --- | --- | --- |
| Roof Type |  |  |  |  |
| Degree of Enclosure |  |  |  |  |
| System for grass |  |  |  |  |
| Roof Covering |  |  |  |  |

|  | Choice | Total Value Added | Cost | Difference (Value added – Cost) |
| --- | --- | --- | --- | --- |
| Roof Type |  |  |  |  |
| Degree of Enclosure |  |  |  |  |
| System for grass |  |  |  |  |
| Roof Covering |  |  |  |  |